## Slide 1: How to Buffer?
Parvin Taheri
March, 2019
Cisco Systems

## Slide 2: Simple model of TCP throughput dynamics
Good Throughput
Increasing TCP Window
“knee”
“cliff”
Bottleneck Capacity
Queue
Depth
Notes: Effective Window: the amount of data TCP sends each RTT
Knee: the lowest window that makes throughput approximate capacity
Cliff: the largest window that makes throughput approximate capacity
Note that throughput is the same at knee and cliff. Increasing the window merely increases RTT, by increasing queue depth
Yes, there is a more complex equation that takes into account loss.
It estimates throughput above the cliff.

## Slide 3: Review: TCP Congestion Control
Rule for adjusting W
  If an ACK is received: W ← W+1/W
  If a packet is lost: W ← W/2
Only W packets may be outstanding
Source
Dest
t
Window size
  Packet loss serves as a rate regulator

## Slide 4: Data Center Specific

## Slide 5: Data Center Workload is Strongly Heavy-Tailed
Most flows are small; but most of the traffic is sent by a small number of flows

## Slide 6: Data Center Transport
But the flows are diverse:
Short flows
(e.g., query, coordination)
Large flows
(e.g., data update)
Low Latency
High Throughput
Goal: Complete “flows” quickly
Notes: So the ultimate goal of data center transport is to complete these internal transactions or “flows” as quickly as possible.
What makes this challenging is that the flows are actually quite diverse. In particular, there are…
And these different flows require different things to complete quickly. For the short flows, we need to provide low latency…

## Slide 7: Buffer requirement
Elephants, relatively small buffers (Bandwidth Delay Product ~ hundreds of KB) are sufficient for TCP to achieve high throughput.
  Buffering increases latency without improving throughput
  Loss helps TCP elephants to regulate its rate
Mice requirement depends on workload (load, burst sizes, arrival pattern, synchronization)
  No time for TCP to react to congestion
  Loss and delay can be detrimental for mice
Notes: Problem: Elephants steal buffer from mice!
How to balance?

## Slide 8: N9K Intelligent Buffer Solutions

## Slide 9: Regulate Elephants and Speed up Mice
Approximate Fair Drop (AFD):
  Elephant flows are regulated with random early drops/marks
  Healthy dose of drops helps TCP to find its bottleneck rate
  Fair bandwidth allocation among elephant flows
Dynamic Packet Prioritization (DPP):
  Mice flows are transferred as a higher priority
  Losses are avoided as much as possible
Notes: Expediting mice flows while regulating elephant flows

## Slide 10: AFD (Approximate Fair Drop)
Buffer Headroom for Mice Flows
AFD Discard/Mark Threshold for Elephant Flows
Apply flow-aware, random, early and fair drops/marks to elephant flows
Protect and preserve buffer headroom for mice flows

## Slide 11: AFD (Approximate Fair Drop)
AFD uses Elephant Trap to identify elephant flows vs mice flows (a flow with a size > M bytes is an elephant)
Only elephant flows are subject to drop/mark
Elephant flows are tracked precisely of their arrival rates and compared against a calculated fair rate to decide drop amount
Elephant flow table also uses a time-out timer (10msec) to remove idle elephants

## Slide 12: DPP (Dynamic Packet Prioritization)
Prioritized Packets
Express Lane
Normal Lane
Egress Queue
Large Flow
Small Flow
Packets beyond the prioritization threshold go through the normal lane.
DPP creates an express lane for mice flows
Mice flows are protected and prioritized to avoid dropping and queuing latency
Elephant flows go through the normal queuing and scheduling

## Slide 13: DPP (Dynamic Packet Prioritization)
DPP uses a packet-count-based threshold to prioritize mice flows (5-tuple)
If the DPP packet threshold is N packets, the first N packets in a flow will be prioritized and sent through a priority lane.
Once the number of packets in a flow reaches the threshold N, the subsequent packets in the flow will go to the normal queue and not be prioritized any more
As a result, mice flows (packets < N) will be always prioritized
DPP uses a time-out timer (10msec) to remove idle flows

## Slide 14: Lab Evaluation Topology
Spine 0
Spine 1
Leaf 0
Leaf 1
H
H
H
H
24x10G
24x10G
4x40G
4x40G

## Slide 15: Lab Setup
Background traffic : real data mining traffic stats (strongly heavy-tailed)
Many to many traffic pattern
We compare the flow completion time (FCT)
  Cisco: 5MB per port, AFD+DPP
  Different vendor: 50+MB per port, (never) Tail Drop

## Slide 16: Breakdown of Flow Completion Time (<100KB)
Chart: Average of Small Flows (< 100KB)
| 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 95.0
5MB: AFD+DPP | 0.24 | 0.24 | 0.24 | 0.24 | 0.24 | 0.24 | 0.25 | 0.25 | 0.25
50+MB: (never) Tail Drop | 0.62 | 1.68 | 2.61 | 4.52 | 7.68 | 10.5 | 13.62 | 18.08 | 21.37

## Slide 17: Breakdown of Flow Completion Time (>10MB)
Chart: Average of Large Flows (> 10MB)
| 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 95.0
5MB: AFD+DPP | 282.92 | 367.76 | 389.86 | 488.8 | 626.39 | 931.6 | 1294.57 | 1840.94 | 2309.59
50+MB: (never) Tail Drop | 268.9 | 343.21 | 364.62 | 445.92 | 590.74 | 900.96 | 1236.83 | 1765.7 | 2328.41
Notes: Zero drops reported for 50MB.
Window max is increased by a lot.
The window max was limited. What’s the point of having big buffer when it is not used because tcp window is capped.
By reducing the timeout of tcp, the cost of a single drop is less than the latency caused by large buffering.

## Slide 18: 1500:1 Incast + Data Mining Background - Scenario from one major cloud provider
Omnet++ Simulation

## Slide 19: Simulation Topology
Spine 0
Leaf 0
Leaf 6
H
H
H
250x40G
10x100G
10x100G
1500:1 Incast+Background
Spine 1
Leaf 1,2,3,4,5

## Slide 20: Traffic
Delay and drop sensitive incast traffic: 1500:1
Each flow is 5KB-10KB  Total incast size is 7.5MB-15MB.
Within time x and x+1ms, all 1500 servers begin brand new TCP sessions
Every 50ms, the incast event is repeated.
Background traffic: data mining (statistics from VL2 paper)
Notes: Each fanout has 5-10KB

## Slide 21: Buffer Size
25MB: Naïve Buffering (Tail Drop)
40MB: Intelligent Buffering (AFD+DPP)
250MB: Naïve Buffering (Tail Drop)

## Slide 22: 1500:1 Incast Completion Time - Average
Chart: Average of Incast Event
| 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0
25MB: Tail Drop | 23.0074 | 17.9204 | 23.8352 | 16.91 | 26.2471 | 27.0575 | 30.0386
250MB: Tail Drop | 7.0926 | 10.3783 | 15.5211 | 13.8049 | 23.1505 | 17.9557 | 17.9417
40MB: AFD+DPP | 4.0073 | 3.4692 | 2.8489 | 5.4442 | 4.1765 | 6.7065 | 9.5066
Notes: At 90% load:
Drop:
250MB
2.3K Incast
25MB
118K Incast

## Slide 23: Data Mining Traffic as Background -Small
Chart: Background Traffic Average for Small Flows (<1MB)
| 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0
25MB: Tail Drop | 1.8022 | 2.9596 | 2.3555 | 1.4208 | 3.5574 | 3.6461 | 4.0411
250MB: Tail Drop | 3.9713 | 8.8168 | 12.855 | 12.446 | 15.6364 | 17.8648 | 16.484
40MB: AFD+DPP | 0.20709 | 0.25145 | 0.22377 | 0.29715 | 0.30581 | 0.27654 | 0.3962
Notes: At 90% load:
Drop:
250MB
2.3K Incast
16K Background
25MB
118K Incast
204K Background

## Slide 24: Data Mining Traffic as Background - Large
Chart: Background Traffic Average for Large Flows (>10MB)
25MB: Tail Drop | 71.1893 | 86.6366 | 102.9879 | 110.7901 | 181.8357 | 230.9167 | 308.4308
250MB: Tail Drop | 68.9692 | 85.7497 | 112.0457 | 117.8692 | 189.3396 | 260.3506 | 335.7405
40MB: AFD+DPP | 71.2956 | 82.7823 | 75.054 | 128.7561 | 109.7758 | 120.9774 | 182.4973
Notes: At 90% load:
Drop:
250MB
2.3K Incast
16K Background
25MB
118K Incast
204K Background

## Slide 25: Summary
Sufficient and intelligent buffering allow mice and elephant flows share network buffers gracefully
N9K switches allows orders of magnitude better performance for mission critical flows without slowing down the elephants flows