## Slide 1: OpenFlow Deployment Anecdotes and Solutions David Erickson Stanford University October 17th, 2011
Notes: Hi my name is David Erickson, I am a PhD candidate in Professor Nick McKeowns research group here at Stanford University.
I’ve been involved with OpenFlow as a consumer of the protocol and assisting with its development and standardization for just under 4 years now. I am also the author of the Beacon OpenFlow controller that hopefully some of you used today, and also maintain the OpenFlowJ Java library.
I hope in this brief talk I can share a few of the nuggets of wisdom I’ve found while working on OpenFlow deployments, as well as describe a couple interesting problems I’ve run into recently. Now their solutions as presented may sound straightforward and obvious, however I assure you when armed only with wireshark and a server log to debug a complex networked system, they are anything but straightforward or obvious. Lets get started:

## Slide 2
Datacenter Network Research Cluster
Beacon
(OF Controller)
160 Servers XenServer 5.6
20 Hardware OpenFlow Switches
160 Software OpenFlow Switches
Non-OpenFlow
OpenFlow

## Slide 3: Gotchas
Flooding
Inband switch control
Performance

## Slide 4: Flooding Gotchas
OpenFlow does not provide spanning tree
Plan for topology with loops or multiple external net connections
DNRC filters out all broadcast packets
  ARP bcast -> unicast module for known hosts
  DHCP bcast -> unicast module
  Hosts send gratuitous ARPs every 60s for discovery

## Slide 5: Flooding Gotchas
Problem #1: Hosts appeared to be bouncing around the network

## Slide 6
Problem #1 Host to Internet
Beacon
(OF Controller)
Non-OpenFlow
OpenFlow

## Slide 7: Flooding Gotchas
Problem #1: Hosts appeared to be bouncing around the network
Issue: MAC timeout at the non-OpenFlow switch

## Slide 8
Problem #1 ARP timeout
Beacon
(OF Controller)
Non-OpenFlow
OpenFlow
MAC Entry
Timeout

## Slide 9: Flooding Gotchas
Problem #1: Hosts appeared to be bouncing around the network
Issue: MAC timeout at the non-OpenFlow switch
Solution: Static MAC mapping on switch plus fallback ingress MAC filtering in Beacon

## Slide 10: Inband Gotchas
Problem #2: Gratuitous ARPs from Hosts never making it to controller, fine from VMs
Issue: Open vSwitch inband algorithm auto forwarded them with ‘hidden’ tables/rules
Solution: Modified inband algorithm to be more selective on the ARPs it auto forwards

## Slide 11: Inband Gotchas
Problem #3: Open vSwitch timing out and reconnecting every few minutes
Particularly challenging
Symptoms:
  OVS log/wireshark showed echo request being sent, but never replied to
  Beacon log showed incoming echo request and immediate replys sent

## Slide 12
Problem #3 OVS disconnecting
Beacon
(OF Controller)
Non-OpenFlow
OpenFlow
Echo
Req
Echo
Rep
ARP
Req
ARP
Req
ARP
Timeout

## Slide 13: Inband Gotchas
Problem #3: Open vSwitch timing out and reconnecting every few minutes
Issue: ARP timeout on controller machine resulted in ARP requests being encapped and returned to controller
Solution: Static ARP entries on controller, could also add static entries to always deliver ARP requests

## Slide 14: Performance Gotchas
Benchmark hardware under expected use case
Slow switch CPU can cause:
  Unexpected delays, packets popping up in odd places
  Switch livelock
  Slow steady state convergence
DNRC source routes based on VLAN tag with some reactive routing in host’s OVS