## Slide 1: Software Defined Networks and the Maturing of the Internet
Nick McKeown
Stanford University

## Slide 2
Notes: Recently you will have heard the Internet is 20 years old…..
When you think of the Internet, you probably think about how you use it, such as using Google to search for information, Facebook to stay in touch with friends, and Netflix or YouTube to watch videos. At some level you are probably aware that the data is coming to you from some distant warehouse full of computers <click> in a series of packets <click>.
But today I won’t be talking about the applications and services we use on top of the Internet. I’m talking about the Internet itself. The Internet infrastructure, the invisible layer of plumbing that sits underneath the applications we all use. It is a sign of the success of the Internet that we don’t normally think about how it works – it’s invisible. We don’t normally think how the water flows through the plumbing when we let the plug out of the bath or flush the toilet. Nor should we need to think about how packets flow and are controlled.
But if we are to understand how the Internet is changing and maturing, we need to think about how data flows, and the decisions people made about how it works. We call these decisions the architectural principles of the Internet, and I’ll be coming to them shortly.
So just for today, we’re going to make the Internet plumbing a first class citizen….

## Slide 3: Why was an Internet so simple and dumb so successful?
Notes: You may be wondering why the Internet designed this way.
Why was an Internet so SIMPLE, DUMB and UNRELIABLE so successful?

## Slide 4: The Internet was successful because it was simple and dumb
Notes: Today it’s pretty widely accepted that the internet was successful precisely BECAUSE it was SIMPLE, DUMB and UNRELIABLE!
So how can that be?

## Slide 5
David D. Clark
Chief Protocol Architect, Internet
1981 - 1989

## Slide 6: Architectural Principles
Dumb and simple
i
Streamlined, fast, low-cost, easy to maintain, infrequent upgrades.
Reliable in-order delivery can be built on top, at the end-points.
i
Intelligent end-points (computers).
1
2

## Slide 7: Architectural Principles
Decentralized control
i
Rapid organic growth
1969
3
Notes: : Four nodes
UCLA, SRI, UCSB, Utah.

## Slide 8
The Opte Project
Notes: Clearly this is way beyond something a human can do in their head. (Well, me at least – maybe you can).
So we need automated algorithms to calaculate the route and put the necessary fwding entries into the forwarding tables in the routers.
To calculate the routes, the routers will exchange information with each other about the current topology.
This is the job of what we call the Routing Algorithm or the Routing Protocol.
In some cases, the algorithm to calculate the route is wrapped in with the exchange of the state. In other cases, they are separate.
WE will look at both.

## Slide 9: Computers connected to Internet
Chart: 
| 41475.0 | 41294.0 | 41110.0 | 40928.0 | 40744.0 | 40563.0 | 40379.0 | 40198.0 | 40014.0 | 39833.0 | 39649.0 | 39467.0 | 39283.0 | 39102.0 | 38918.0 | 38737.0 | 38553.0 | 38372.0 | 38188.0 | 38006.0 | 37641.0 | 37457.0 | 37276.0 | 37092.0 | 36911.0 | 36727.0 | 36545.0 | 36360.0 | 36179.0 | 35995.0 | 35814.0 | 35630.0 | 35449.0 | 35265.0 | 35083.0 | 34899.0 | 34718.0 | 34534.0 | 34353.0 | 34169.0 | 33988.0
 | 996230757 | 963518598 | 908585739 | 888239420 | 849869781 | 818374269 | 768913036 | 732740444 | 681064561 | 625226456 | 570937778 | 541677360 | 489774269 | 433193199 | 439286364 | 394991609 | 353284187 | 317646084 | 285139107 | 233101481 | 171638297 | 162128493 | 147344723 | 125888197 | 109574429 | 93047785 | 72398092 | 56218000 | 43230000 | 36739000 | 29670000 | 19540000 | 16146000 | 12881000 | 9472000 | 6642000 | 4852000 | 3212000 | 2217000 | 1776000 | 1313000
Source: ISC
Millions
1 Billion

## Slide 10: The Internet was deliberately designed …
To be simple and streamlined.
To have decentralized control: Lots of individually controlled pieces.
Which led to …
Explosive organic growth of the Internet.
A great business for companies selling routers.
simple and streamlined
A great business
Notes: About $100B per year. 70% gross profit margin. Which means for every $100 of goods sold, they cost $30 to build. Not bad.
There is a business paradox here. Or rather, the situation is not stable: Simple and Streamlined is at odds with “A great business” <click>
There are two ways to break the instability: Either the Internet becomes a simple and streamlined commodity and is not particularly profitable. This would have been the social good.
Or, we break the simple and streamlined to justify keeping the profit margins high, and keeping others out of the business.
Which would you do if you had a very successful, great business?

## Slide 11: Number of published Internet Standards
Chart: 
Notes: First one published April 7, 1969
Many of these are written and published by the router companies themselves…..

## Slide 12: Cisco Stock Price
1991
1999
200x
Google Finance

## Slide 13
50+ million lines of code
Tens of billions of gates
Routers are fragile, insecure, bloated and power hungry
Like the computer mainframes of the 1980s.
“Great business” triumphed over “simple and streamlined”.
Hardware
Software
Notes: The consequence: Routers bloated, expensive, fragile and insecure….
We can argue about the details; but it couldn’t be any other way, because the market is making it so.
So what to do?

## Slide 14: Computers became easier to use and more reliable…
1960s
1960s
1980s
1980s
2000s
Now
2000s
Now

## Slide 15: Making Software Work
Static Code Analysis
Invariant
Checker
Interactive Debugger
Model Checking
Run-time Checker
Specification
Testbench
Functional Description (Code)
$10B tool business supports a $300B S/W industry
100s of Books
>100,000 Papers
10s of Classes

## Slide 16: Networks became harder to manage and less reliable…
Now
Now

## Slide 17: Making Networks Work (Today)
traceroute, ping, tcpdump, SNMP, Netflow
…. er, that’s about it.

## Slide 18: Networks are kept working by “Masters of Complexity”
A handful of books
Almost no papers
No classes

## Slide 19: What this means for people who own large networks

## Slide 20: Example 1: Internet Service Providers
Global IP traffic growing 40-50% per year
End-customer monthly bill remains unchanged
Therefore, cost of ownership needs to reduce 40-50% per Gb/s per year
But in practice, reduces by <20% per year
£20/month
time
Growth in traffic
Revenue
Total cost

## Slide 21: Example 2: Data Center Owner
Cost
400,000 servers
20,000 switches
$5k per switch = $100M
$1k commodity switch = $20M
Savings in 10 data centers = $800M
Control
More flexible control
Tailor network as needed
Quickly improve and innovate

## Slide 22: Sidebar: Lessons from the computer industry

## Slide 23: Hardware

## Slide 24: 2000: Rack-mounted Servers
Dell Servers
HP Servers

## Slide 25: 2005: The whitebox server
DRAM
Sheet metal
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 27: Dell Stock Price
Google Finance
$42
$14
2005
2013

## Slide 28: Software

## Slide 29: “Software will eat the world”
Marc Andreessen

## Slide 30: Software in 2014
Smartphone: Open 75%, Closed 25%
Browser: Open 63%, Closed 37%
Websites: Open 67%, Closed 33%
DC servers: Open 70%, Closed 30%
Tablet: Open 62%, Closed 38%
Mainframes: Open 60%, Closed 40%
Supercomputers: Open 99%
Open-source still growing fast

## Slide 31: CPU + Linux + Application
DRAM
Sheet metal
Programmable
Hardware
Linux
Open Source
Software
App
App
App
Proprietary
Software
Notes: 2.5Billion transistors --- 100,000 times bigger. 4GHz --- 10,000 times faster
Taiwan

## Slide 32: CPU + Linux + Application
Search
Facebook
YouTube
Netflix
Amazon
Network:
Baremetal
xChip/x86 + Linux
(500 thousand/yr)
Compute:
Baremetal
x86 + Linux
(10 million/yr)
Public Internet
Telcos/Cable
Open
Connect
B4
Swan
Google Fiber
Google WiFi
ARM + Linux
Baremetal
xChip/x86 + Linux/BSD

## Slide 33: (End of Sidebar: Lessons from the computer industry)

## Slide 34: SDN: What just happened?
Rise of Linux.
Rise of merchant switching silicon.

## Slide 35
Rise of Switch Chips (“xChips”)
1994
Linux v1
IBM, Compaq, Dell run Linux
1998
v2
1996
Android Linux
>75% new smartphones
2013
2011
OCP
Server
OCP
Switch
ONIE
OCP
Wedge
ODL
1st xChip +
Linux DC
2008
1st xChip +
Linux WAN
2012
2014
ONL
ONOS
OpenNFV
Google incorporated
OVS
2010
NSX
Cisco 2014
#1 competitor = software company (VMware) #1 fear = bare-metal switches
Virtual Ethernet ports
> Physical ports

## Slide 36: The bare-metal switch
DRAM
Sheet metal
xChip

## Slide 37: OCP: Wedge switch (open-source design)
BCM xChip: 1.2Tb/s

## Slide 38: Bare-metal Switch Software
Boot Loader
Switch OS
API/Driver
Forwarding
Agent
Environment
Agent
Fans, connectors, power supply
CPU
Switch
Chip
Config
Open-source
ONIE
Open-source
ONL
Open-source
OF-DPA
Open-source
FBOSS, OVS,
Switch Light, Indigo.

## Slide 39: Will switches be hardware or software?

## Slide 40: Packet Forwarding Speeds
Chart: 
| 1990.0 | 1995.0 | 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0
Switch Chip | 0.4 | 8 | 10 | 100 | 640 | 3200 | 14000
CPU | 0.1 | 1 | 2 | 5 | 20 | 80 | 200
Fixed/microcoded
Fixed, closed
Programmable,
open
Gb/s
(per chip)
3.2Tb/s

## Slide 41: Packet Forwarding Speeds
Chart: 
| 1990.0 | 1995.0 | 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0
Switch Chip | 0.4 | 8 | 10 | 100 | 640 | 3200 | 14000
CPU | 0.1 | 1 | 2 | 5 | 20 | 80 | 200
Fixed/microcoded
Fixed, closed
Programmable,
open
50x
3.2Tb/s
Gb/s
(per chip)

## Slide 42: Switches will be built from programmable ASICs

## Slide 43
Boot Loader
Switch OS
API/Driver
Forwarding
Agent
Environment
Agent
Optional Remote API
(Remote) Network Controller
Config
Open-source
ONIE
Open-source
ONL
Open-source
OF-DPA
Open-source
P4
Open-source
FBOSS, OVS,
Switch Light, Indigo.
Open-source
ONOS, ODL
NOX, POX, Ryu
Floodlight, Beacon
Fans, connectors, power supply
CPU
Switch
Chip

## Slide 44
Server
Switch
Radio
VM
Linux
Linux
Linux
Linux
Routing, Traffic Engineering,
Mobility, VPN
Programmable
Hardware
Open Source
Software
Proprietary
Software
PIC
Linux
Network OS (SDN, NFV, …)
DPI, Load Balance, SPAM
New Services
System Management

## Slide 45: What just happened?
Rise of Linux.
Rise of merchant switching silicon.
Slow glide of box vendors to irrelevance.
Network owners just got handed the keys!

## Slide 46: Computer Industry
Specialized
Operating System
Specialized
Hardware
Specialized
Applications
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Microprocessor

## Slide 47: Networking Industry
Switch Chips
Specialized
Operating System
Specialized
Hardware
Specialized
Features
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Open Interface
Control Plane 1
Control Plane 2
NOX
Beacon
ONIX
POX
ONOS
Flood light
Trema
ODL
Ryu

## Slide 48
“Because there is no army that can hold back an economic principle whose time has come.”
John Donovan, AT&T

## Slide 49: Summary
Network infrastructure will be:
  Proprietary software (to differentiate)
  Open-source software infrastructure
  Programmable hardware substrate
Existing box vendors will turn into software vendors, or they will be irrelevant (and disappear)

## Slide 50: Three consequences of SDN
Virtualized networks: Already started to happen (the “killer app”)
More programmable networks: New programmable forwarding devices
More reliable networks: “Top down” programmability enables formal network verification

## Slide 51: Even simple questions are hard
Can host A talk to host B?
What are all the packets from A that can reach B?
Are there any loops in the network?
Is Group X provably isolated from Group Y?
What happens if I remove a line in a config file?

## Slide 52: More interesting questions
When I add a new forwarding rule, how can I dynamically check in real-time if it will violate my network policy?
How do I track down the source code that was the root cause of a data plane error?
If switch hardware is malfunctioning, how will I know? How will I identify the switch/rule?

## Slide 53: Neither observe nor control
Complex interaction
  Between multiple protocols on a switch/router.
  Between state on different switches/routers.
Multiple uncoordinated writers of state.
Network owner can’t…
  Observe all state.
  Control all state.

## Slide 54: Header Space Analysis: Modeling Forwarding Behavior

## Slide 55: Header Space Analysis [NSDI ‘12]
A
B
L
Header
Data
01110011…1
Header
Data
111..100000

## Slide 56: Header Space Analysis
1
2
Match + Action

## Slide 57: The set of packets from A that can reach B
A
B

## Slide 58: All packets from A that can reach B
A
B

## Slide 59: Implications
Reachability and loops
Prove two groups are isolated
Regardless of protocol or layer
Analogy to Boolean algebra
Follow-on
  NetPlumber: Dynamic checking for Google’s OpenFlow WAN 10,000 times per second
  ATPG: Testing every forwarding rule 10-times per second

## Slide 60: <The End>