## Slide 1: Programmable forwarding planes are here to stay
Nick McKeown
Stanford University

## Slide 2: SDN Act 1
In which network owners take
charge of their control plane

## Slide 3: Computer Industry
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Applications
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Disaggregation
Microprocessor

## Slide 4: Networking Industry
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Features
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Open Interface
Control Plane 1
Control Plane 2
NOX
Beacon
ONIX
POX
ONOS
Flood light
Trema
ODL
Ryu
Merchant Switch Chips
Disaggregation

## Slide 5: SDN inevitable because…
Rise of Linux.
Rise of whitebox servers and data centers.
Rise of merchant switching silicon.

## Slide 6
Applications
OS
CPU
x86
Applications
Linux
Applications
OS
CPU + ASIC
x86 + ASIC
Control Programs
Linux
Servers
Network switches
Legacy
Whitebox
Legacy
Whitebox

## Slide 7: Example: Big Data Center
Cost
500,000 servers
25,000 switches
$10k per legacy switch = $250M
$2k disaggregated switch = $50M
Savings in 5 data centers = $1Bn
Control
Centralized remote control is easier
“Centralize if you can, distribute if you can’t”
Customized, differentiated network
Home grown traffic engineering
50% utilization → 95% utilization

## Slide 8: All networking equipment is disaggregating
Basestation
5G GW
Optical and Metro Transport
WiFi AP
Residential broadband access
Enterprise network equipment: switch, router, firewall
“Software is eating the world (of networking)”

## Slide 9
Rise of Merchant Switch Chips
1994
Linux v1
IBM, Compaq, Dell run Linux
1998
v2
1996
Android/Linux
3/4 new smartphones
2/3 servers
2/3 websites
2/3 mainframes
99% supercomputers
2013
2011
OCP
Server
OCP
Switch
ONIE
ODL
1st MSDC with switch chip + Linux
2008
1st WAN with
Switch chip + Linux
2012
2015
ONL
ONOS
OpenNFV
Google incorporated
OVS
2010
NEC
+
HP
# Virtual Ethernet ports
> # Physical ports
ONAP
2016
HP
Open
Switch
OVN
SONiC
OCP
Wedge
FBOSS
dNOSS
2017/8
Stratum
CORD
P4
Runtime

## Slide 10: Now I can tailor my network to meet my needs!
I can….
Quickly deploy new protocols.
Monitor precisely what my forwarding plane is doing.
Fold expensive middlebox functions into the network, for free.
Try out beautiful new ideas. Tailor my network to meet my needs.
Differentiate. Now I own my intellectual property.

## Slide 11: But wait a minute…

## Slide 12
New
Switch OS
Driver
OSPF
BGP
etc.

## Slide 13
Network Equipment Vendor
Network Owner
ASIC
Team
Software
Team
Feature
Weeks
Years
Years
Feature
Feature

## Slide 14: When you need a new feature…
Equipment vendor can’t just send you a software upgrade
New forwarding features take years to develop
By then, you’ve figured out a kludge to work around it
Your network gets more complicated, more brittle
Eventually, when the upgrade is available, it either
  No longer solves your problem, or
  You need a fork-lift upgrade, at huge expense.

## Slide 15: Network systems are built “bottoms-up”
Switch OS
Fixed-function switch
Driver
“This is how I process packets …”

## Slide 16: “Programmable switches are 10-100x slower than fixed-function switches”
Conventional wisdom in networking

## Slide 17: SDN Act 2
In which network system developers take
charge of their forwarding plane too

## Slide 18: Network systems are starting to be programmed “top-down”
Programmable Switch
Driver
Switch OS
“This is precisely how you must process packets”

## Slide 19: Why are programmable forwarding planes happening now?

## Slide 20: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
Networking
?
Language
Compiler
>>>

## Slide 21: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
PISA
Networking
P4
Compiler
>>>

## Slide 22
Match+Action Stage
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
PISA: Protocol Independent Switch Architecture

## Slide 23
PISA: Protocol Independent Switch Architecture

## Slide 24: Example P4 Program
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
Header and Data Declarations
Parser Program
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
Tables and Control Flow
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }

## Slide 25: To learn more, visit P4.org

## Slide 26: Barefoot Tofino 6.5Tb/s Switch December 2016
The world’s fastest switch in production.
Forwarding defined in software (P4).
Programs always run at line-rate.
Same power.
Same cost.

## Slide 27: How programmability is being used
Reducing complexity
1

## Slide 28: Reducing complexity
Compiler
Programmable Switch
Driver
Switch OS
switch.p4
IPv4 and IPv6 routing
- Unicast Routing
- Routed Ports & SVI
- VRF
- Unicast RPF - Strict and Loose
- Multicast
- PIM-SM/DM & PIM-Bidir
Ethernet switching
- VLAN Flooding
- MAC Learning & Aging
- STP state
- VLAN Translation
Load balancing
- LAG
- ECMP & WCMP
- Resilient Hashing
- Flowlet Switching
Fast Failover
– LAG & ECMP
Tunneling
- IPv4 and IPv6 Routing & Switching
- IP-in-IP (6in4, 4in4)
- VXLAN, NVGRE, GENEVE & GRE
- Segment Routing, ILA
MPLS
- LER and LSR
- IPv4/v6 routing (L3VPN)
- L2 switching (EoMPLS, VPLS)
- MPLS over UDP/GRE
ACL
- MAC ACL, IPv4/v6 ACL, RACL
- QoS ACL, System ACL, PBR
- Port Range lookups in ACLs
QOS
- QoS Classification & marking
- Drop profiles/WRED
- RoCE v2 & FCoE
- CoPP (Control plane policing)
NAT and L4 Load Balancing
Security Features
- Storm Control, IP Source Guard
Monitoring & Telemetry
Ingress Mirroring and Egress Mirroring
Negative Mirroring
Sflow
INT
Counters
Route Table Entry Counters
VLAN/Bridge Domain Counters
Port/Interface Counters
Protocol Offload
- BFD, OAM
Multi-chip Fabric Support
- Forwarding, QOS

## Slide 29: Reducing complexity
Compiler
Driver
Switch OS
My switch.p4
Programmable Switch

## Slide 30: How programmability is being used
Adding new features
2

## Slide 31: Protocol complexity 20 years ago
Ethernet
IPv4
IPX
ethtype
ethtype

## Slide 32
Datacenter switch today
switch.p4

## Slide 33: Adding features: Some examples so far
New encapsulations and tunnels
New ways to tag packets for special treatment
New approaches to routing: e.g. source routing in MSDCs
New approaches to congestion control
New ways to process packets: e.g. processing ticker-symbols

## Slide 34: New applications: Some examples so far
Layer-4 Load Balancer1
  Replace 100 servers or 10 dedicated boxes with one programmable switch
  Track and maintain mapping for 5-10 million http flows
Fast stateless firewall
  Add/delete and track 100s of thousands of new connections per second
Cache for Key-value store2
  Memcache in-network cache for 100 servers
  1-2 billion operations per second
[1] “SilkRoad: Making Stateful Layer-4 Load Balancing Fast and Cheap Using Switching ASICs.” Rui Miao et al. Sigcomm 2017.
[2] “NetCache: Balancing Key-Value Stores with Fast In-Network Caching”, Xin Jin et al. SOSP 2017

## Slide 35: How programmability is being used
Network telemetry
3

## Slide 36
“Which path did my packet take?”
1
“I visited Switch 1 @780ns, Switch 9 @1.3µs, Switch 12 @2.4µs”
“Which rules did my packet follow?”
2
“In Switch 1, I followed rules 75 and 250. In Switch 9, I followed rules 3 and 80. ”
# | Rule
1 | 
2 | 
3 | 
… | 
75 | 192.168.0/24
… | 

## Slide 37
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4

## Slide 38
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4
Aggressor flow!

## Slide 39: We’d like the network to answer these questions
“Which path did my packet take?”
“Which rules did my packet follow?”
“How long did it queue at each switch?”
“Who did it share the queues with?”
A PISA device programmed using P4 can answer all four questions at line rate, for the first time. Without generating additional packets.
1
2
3
4

## Slide 40: INT: Inband Network Telemetry
Log, Analyze
Replay
Add: SwitchID, Arrival Time, Queue Delay, Matched Rules, …
Original Packet
Visualize

## Slide 41
Log, Analyze
Replay
Visualize
/* INT: add switch id */
action int_set_header_0() {
add_header(int_switch_id_header);
modify_field(int_switch_id_header.switch_id,
global_config_metadata.switch_id);
}
/* INT: add ingress timestamp */
action int_set_header_1() {
add_header(int_ingress_tstamp_header);
modify_field(int_ingress_tstamp_header.ingress_tstamp, i2e_metadata.ingress_tstamp);
}
/* INT: add egress timestamp */
action int_set_header_2() {
add_header(int_egress_tstamp_header);
modify_field(int_egress_tstamp_header.egress_tstamp,
eg_intr_md_from_parser_aux.egress_global_tstamp);
}
P4 code snippet: Insert switch ID, ingress and egress timestamp

## Slide 42: How programmability is being used
3
2
Reducing complexity
Adding new features
Network telemetry
1

## Slide 43: In summary…
SDN is about who is in charge!
  Act 1: Network owners and operators took charge of how their networks are controlled.
  Act 2: They also decide how packets are processed.
Chip technology: Programmable forwarding now has the same power, performance and cost as fixed function.
New ideas: Beautiful new ideas now owned by the programmer, not the chip designer.

## Slide 44: Thank you!