## Slide 1
ATRIUM
Open SDN Distribution
Saurav Das
Principal System Architect, ONF
With contributions from ONF Atrium Management team and many others …

## Slide 2
Project Atrium Goals
Integration
  Create vertically-integrated open-source stacks
  From open-source components, OF1.3 & Hardware
  Enable network operators to download distribution
  from a single location
Interoperability
  Enable multiple hardware vendors to plugin to stack
  Allows end-users to select different hardware classes
  for common use-cases.
Deployments
  Work hand-in-hand with operators on deployable use
  cases leading to trials.
  - Give operators confidence in pure SDN solutions

## Slide 3
SDN Provides a Lot of Choices

## Slide 4
Solution: Vertically Integrated Stack
== SDN Distribution

## Slide 5
ONOS
What is Atrium today?
vlan x
vlan y
vlan z
E-BGP
E-BGP
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
BRCM SDK API
OCP: Open Compute Project; ONL: Open Network Linux; ONIE: Open Network Install Env;
BRCM: Broadcom Merchant Silicon ASICs; OF-DPA: OpenFlow Datapath Abstraction
OFDPA Driver
Peering Application
Quagga BGP
Accton 5710
Quanta LY2

## Slide 6
What is Atrium today?

## Slide 7
A Closer Look at Interoperability
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
Different combinations of
Match-Action Tables form
Different OF 1.3 pipelines
How can a controller manage these differences?
How can an application work across these differences?

## Slide 8
SDN Application
Flow Objectives
OFDPA Driver
Controller
Switch
OpenFlow 1.3
OpenFlow 1.3
Write the app once
without pipeline details
adapt to specific
Pipeline using
device driver
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
SoftRouter Driver
Corsa Driver
Pica8
Driver
Centec Driver
Solution: Flow Objectives API

## Slide 9: Example: Filtering Objective
Filter  only Permit or Deny options
On match fields of packet header
Router port: X
Permit: MAC 1, VLAN 1, IP 1, 2, 3
Permit: MAC 1, VLAN 2, IP 4, 5
Corsa Driver
OF-DPA Driver
T0
mac
T2
port-vlan
T4/5
T6
ip
T0
port
T1
Port-vlan
T2
mac
T4
ip
Flow Objectives

## Slide 10: Example: Next Objective
Next  next hop for forwarding
Similar to OF 1.3 group, but …
NEXT- HOP
Corsa Driver
bkt
Indirect group
NoviFlow & Pica8 Drivers
 Flow-actions
bkt
OF-DPA Driver
Group chain
Flow Objectives

## Slide 11: Atrium Demo @ SDN Solution Showcase
V1
Hosts (1.0.0.1)
Hosts (2.0.0.1)
NoviFlow
Accton
Netronome
Q1
Corsa
Quanta
Q2
V2
Pica8
Centec
bgp1> sh ip bgp summary
BGP router identifier 192.168.10.101, local AS number 65000
RIB entries 3, using 336 bytes of memory
Peers 5, using 22 KiB of memory
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
1.1.1.1 4 65000 30090 31109 0 0 0 1d01h43m 0
192.168.10.1 4 65001 31095 31114 0 0 0 1d01h43m 1
192.168.11.1 4 65101 30775 30784 0 0 0 21:07:07 1
192.168.13.1 4 65301 28322 28339 0 0 0 18:11:55 1
192.168.22.1 4 65201 25959 25974 0 0 0 21:23:24 1
Total number of neighbors 5
bgp1> sh ip bgp
BGP table version is 0, local router ID is 192.168.10.101
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 1.0.0.0/24 192.168.10.1 1 0 65001 i
* 2.0.0.0/24 192.168.22.1 0 65201 65202 65203 65002 i
* 192.168.13.1 0 65301 65302 65303 65002 i
*> 192.168.11.1 0 65101 65102 65002 i
Total number of prefixes 2
AS65301
AS65302
AS65201
AS65202
AS65203
AS65000
AS65303
AS65002
AS65102
AS65101
AS65001

## Slide 12: Atrium Pre-release Deployment

## Slide 13: Atrium Post-release Operator Engagements

## Slide 14: What’s Next?
Continued Improvements
  Hardening & Stability
  Performance
  Missing features: untagged, runtime-config, static-routes
  Hardware Automated Test Infrastructure
New Features
  IGP & ECMP support
  Requests from operators (eg. Route filtering)
Other platforms
- OpenDaylight support
https://groups.opensourcesdn.org/wg/Atrium/dashboard
LEARN MORE & JOIN THE COMMUNITY:

## Slide 15
Summary
Integration
  Atrium 1st release brings together ONOS, Quagga, OCP components (ONL, ONIE) and OFDPA with white-boxes + vendor equipment
  Open SDN Distribution (2015/A release: June 30th)
Interoperability
  ONF builds 7 routers!
  Key architectural contribution: Flow Objectives & Device Drivers
Deployments
  Pre release deployment in Sydney.
  More coming as we engage operators
Acknowledgements
  All the switch vendors, ONF management team, ON.Lab support
  Ali Al-Shabibi & Jonathan Hart (ON.Lab)
  Rob Sherwood (Big Switch Networks)