## Slide 1
CORD: Fabric
An Open-Source Leaf-Spine L3 Clos Fabric
Saurav Das
Principal System Architect, ONF
In collaboration with:

## Slide 2
Large number of COs
Evolved over 40-50 years
Huge source of CAPEX/OPEX
Problem: Today’s Telco Central Offices (COs)
Fragmented non-commodity hardware.
Physical install per appliance per site
Nearly 300+ unique deployed appliances.
BNG
Firewall
DPI
CDN
Message
Router
Carrier Grade NAT
Session Border
Controller
PE Router
SGSN/GGSN/PDN-GW
Huge source of CAPEX/OPEX
Not geared for Agility/ Programmability
Does not benefit from Commodity Hardware
Notes: Before I talk about CORD in detail, let me explain the fundamental problem it is solving.
Today’s Central offices house fragmented, non-commodity infrastructure. Each CO hosts more than 300 unique deployed appliances, each requiring a physical install and specialized management.
It’s not surprising then that the Telco central offices are a huge source of CAPEX and OPEX and their design/infrastructure is not geared for programmability and agility.

## Slide 3
IO
IO
Metro Core
Link
IO
Access Link
Fabric
Spine
Switches
Leaf Switches
vBNG
vCPE
vOLT
NFVI Orch- XOS
DHCP
LDAP
RADIUS
Control
Data
PON OLT MACs
Commodity hardware
SDN Control Plane- ONOS
Applications
CORD: Central Office Re-architected as Datacenter
ONT
Simple CPE
GPON
GPON OLT

## Slide 4
Open-Source Leaf-Spine Fabric
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
Open Source
SDN-based
Bare-metal
Slow
I/O:
PON OLT MACs
Access
Links
CORD Pod – up to 16 Racks
Fast
I/O
Metro
Core
Links
HA, scales to 16 racks, OF 1.3, Topo-Discovery, Configuration, GUI, CLI, Troubleshooting, ISSU
Fabric Control Application: Addressing, ECMP Routing, Recovery, Interoperability, API support
ONOS Controller Cluster

## Slide 5
White Box SDN Switch
Leaf Switch
48 x 10G ports downlink to servers
in the same rack (subnet)
10G Base T or 10G SFP+
6 -12 x 40G ports uplink to different spine switches
ECMP across all uplink ports
GE mgmt.
White Box SDN Switch
Spine Switch
32 x 40G ports downlink to leaf switches
40G QSFP+
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
Open-Source Leaf-Spine Fabric
BRCM SDK API

## Slide 6
Learn more:
https://wiki.onosproject.org/display/ONOS/Segment+Routing
SPRING-OPEN
Segment Routing on
Bare Metal Hardware

## Slide 7
First Step: PoC Demo at Solution Showcase
Dell
Dell
Dell
Dell
Dell
Dell
4 racks, 2 servers/rack, Dell 4810 bare metal,
ONOS Cardinal controller cluster
ONOS Controller Cluster
Segment Routed
Fabric Control
SDN controlled
L3 Leaf-Spine Clos fabric.
Dell
Dell

## Slide 8
CORD: Fabric
103

## Slide 9
ECMP Routing

## Slide 10
Policy Driven Traffic Engineering

## Slide 11
Analytics Driven Traffic Engineering

## Slide 12
Analytics Driven Traffic Engineering

## Slide 13
Control Plane Failure Recovery

## Slide 15
Jan’15
June’15
Dec’15
June’16
Dec’16
2017
AT&T and ONOS project
define CORD Solution POC
CORD Lab trials
Lab trials with CORD POD
CORD trial deployments
– phase 2
Service Provider deployments
Deployments by multiple Service Providers
CORD trial deployments
– phase 1
CORD POC demo at ONS
CORD Roadmap – From demo to deployment
Note- these timelines are ON.Lab’s projections and forward looking

## Slide 16
Summary
CORD Fabric
  Open-source
  Spine-leaf architecture: L3 Clos
  Bare metal hardware
  SDN based – no use of distributed protocols
  OF 1.3 multi-tables & ECMP groups
  ONOS cluster controllers
  IP/MPLS network using Segment Routing
  sFlow based analytics for TE of elephant flows
Next?
  Integration with vCPE-vOLT-NFaaS
  Special CORD requirements eg. QinQ
  Pod based deployment requirements eg. BGP peering
  Move to open source hardware i.e OCP/ONL/ONIE/OF-DPA