## Slide 1
Central Office Re-architected
as a Datacenter (CORD)
CORD Fabric
Saurav Das
Principal Architect
Open Networking Foundation

## Slide 2
IO
IO
Metro Core
Link
IO
Access Link
Fabric
Spine
Switches
Leaf Switches
vBNG
vCPE
vOLT
NFVI Orch- XOS
DHCP
LDAP
RADIUS
Control
Data
PON OLT MACs
Commodity hardware
SDN Control Plane- ONOS
Applications
CORD: Central Office Re-architected as Datacenter
ONT
Simple CPE
GPON
GPON OLT

## Slide 3
Open-Source Multi-Purpose Leaf-Spine Fabric
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
White Box
Open Source
SDN-based
Bare-metal
Slow
I/O:
PON OLT MACs
Access
Links
CORD fabric – designed to scale up to 16 Racks
Fast
I/O
Metro
Core
Links
HA, scales to 16 racks, OF 1.3, Topo-Discovery, Configuration, GUI, CLI, Troubleshooting, ISSU
Fabric Control Application: Addressing, ECMP Routing, Recovery, Interoperability, API support
ONOS Controller Cluster
API

## Slide 4
White Box SDN Switch
Accton 6712
Leaf Switch
24 x 40G ports downlink to servers
via 4 X 10G breakout DAC
8 x 40G ports uplink to different spine switches
ECMP across all uplink ports
GE mgmt.
White Box SDN Switch
Accton 6712
Spine Switch
32 x 40G ports downlink to leaf switches
40G QSFP+/DAC
GE mgmt.
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP: Open Compute Project
ONL: Open Network Linux
ONIE: Open Network Install Environment
BRCM: Broadcom Merchant Silicon ASICs
OF-DPA: OpenFlow Datapath Abstraction
Leaf/Spine Switch Software Stack
to controller
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
Open Hardware & Software Stacks
BRCM SDK API

## Slide 5
ONOS
Project Atrium Stack
vlan x
vlan y
vlan z
E-BGP
E-BGP
BRCM ASIC
OF-DPA
Indigo OF Agent
OF-DPA API
OpenFlow 1.3
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
BRCM SDK API
OCP: Open Compute Project; ONL: Open Network Linux; ONIE: Open Network Install Env;
BRCM: Broadcom Merchant Silicon ASICs; OF-DPA: OpenFlow Datapath Abstraction
OFDPA Driver
Peering Application
Quagga BGP

## Slide 6
Field-Trial Specification
Rack 1 Leaf 1
Rack 1 Leaf 2
GE L2 Switch
2 X 10GE
(bonded)
dual-homed server to ToRs (leafs)
1 X GE mgmt
Rack includes
OLTs
Servers
GE L2 Switch
OVS
C
C
VM
Spine 1
Spine 2
40G uplinks
Rack 2 Leaf 1
Rack 2 Leaf 2
2 racks, 2 ToRs/rack, 2 spines, servers dual homed to ToRs

## Slide 7
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 8: The single flow table abstraction
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Rule
Action
Stats
Forward packet to zero or more ports
Encapsulate and forward to controller
Send to normal processing pipeline
Modify Fields
Any extensions you add!
exact/wildcard, + bitmasks for some fields
Packet + byte counters
VLAN
pcp
IP
ToS
…
Notes: Rules: Each rule has a set of fields that it can match on, from Layer 1, the physical port, up to layer 4, the socket port. Each of these can be wildcarded or exact-matched, and some special fields can have bitmasks applied – for example Layer-3 IP prefix matching. You have the option of configuring highly specific rules with exact-match flow entries, very general ones with wildcards, or a mix.
Note that a later field may only have meaning if a previous field had a specific value; for example, a TCP field only makes sense if the IP version is 4.
Actions: Actions encode what to do with a packet. You can drop the packets, send it to one port, or multicast it to multiple ports. You can send it to the controller for further processing. In a hybrid switch, you can even send the packet to a normal processing pipeline. You can modify fields, and even extend the protocol with new actions.
Stats: OpenFlow defines packet and byte counters for each rule, which can be used for accounting, monitoring, flow balancing, or even security purposes.
[TODO: Possibly start with an example of a full wild card and a full exact match flow.]

## Slide 9: Issue #1 with OpenFlow 1.0
Data Path (Hardware)
OpenFlow Client
Vlan
Table
L2
Table
L3
Table
ACL
Table
Small Table Size
128k
32k
2k
Notes: Why is it important to look at 1.0 – because most controllers and switches out there are still 1.0, even though 3 years later we are at v1.4

## Slide 10
Issue #2 with OpenFlow 1.0
Table-space (or flow-space) explosion
  Cross-Product Problem
def:
A condition where multiple independent header fields affect a packet’s forwarding, which forces the use of many flow entries in a single table.

## Slide 11: Issue #2 with OpenFlow 1.0
Table space explosion
A, Y1
A, Y2
A, Y3
A, Y4
A, Y5
B, Y1
B, Y2
B, Y3
B, Y4
B, Y5
C, Y1
C, Y2
C, Y3
C, Y4
C, Y5
OF 1.0 Single Table
A
Y1,
Y2,
Y3,
Y4
Y5
B
C
Single-table abstraction may use table space inefficiently compared to multiple tables
A, B, C, Y could be MAC or IP addresses, VLAN tags, MPLS labels etc.

## Slide 12: Issue #3 with OpenFlow 1.0
Limited match options
Supported:
MAC, VLAN, IP, L4 ports
Missing:
IPv6
QinQ
MPLS
SCTP
Optical circuits
Notes: The second type of issue with OpenFlow 1.0 is the limited set of pre-defined fields, that can’t easily be extended.
The older, more obvious stuff is supported: MAC, VLAN, IP, and L4 ports. But none of the newer WAN and data center stuff is supported, like IPv6, MPLS, and QinQ, or stacked VLAN tags. There’s other stuff you’d like to support, like optical circuit flows, or some arbitrary new version of IP, which the protocol has no way to represent.

## Slide 13: Issue #4 with OpenFlow 1.0
Limited forwarding options
Supported:
broadcast, multicast, drop
Missing:
packet spreading
forwarding to a virtual port
general byte modifications
sw1
sw2
link aggregation
sw1
multipath spreading
sw2
sw3
Notes: The third major limitation is the lack of forwarding options. Basic stuff is supported, like broadcast and multicast and drop, but you can’t easily spread packets across ports.
For example, two links might be aggregated together, but to use those links, you’d have to use a whole bunch of flow entries to spread packets across them. Similarly, you might want to distribute traffic evenly to two destinations.
Ideally, you’d use one entry and it would spread the packets, either round-robin, or based on some content hash.
There are other things you’d like to do, like forward to a virtual port (to implement tunnels), or do general byte modifications.

## Slide 14
state
behavior
Interface
msg
match Eth, VLAN, IP, L4
flows
1.0
Q4 ‘09
single message queue
w/optional barriers
ports
forward {0, 1, n}
1.1
Q1 ‘11
+ Multiple Tables/Pipelines:
+ Group Tables
+ forward 1-in-n (ECMP)
+ match QinQ, MPLS, SCTP
+ match virtual ports
+ extensible match
+ extensible actions
1.2
Q4 ‘11
+ IPv6
+ multiple controllers
1.3
Q2 ‘12
+ per-flow metering
+ tunnel-id
OpenFlow has evolved towards production readiness.
+ multiple channels (auxiliary connections)
1.4
Q4 ‘13
+ optical ports
+ synchronized tables
+ bundle messages
Notes: Fortunately, over time, OpenFlow has evolved to address these all of these limitations that I mentioned.
1.1 was a huge change. Really should have been called 2.0, because it added a multiple-tables model. This enables much more efficient flow table usage, but it raises potential issues with a mismatch between the pipeline you want and the pipeline a device can implement.
1.2 added a bunch of nice extra features:
[explain]
1.3 starts to approach feature completion, where you pretty much have everything you could want, and full extensibility for anything not already there.
[BDH note: I don’t have much to add beyond the names.]

## Slide 15: Multiple Tables in OF1.3
Untyped, Feed-forward, Skip ahead, Early exit
Notes: Don’t take this as gospel. One choice of many. Tries to provide generality for future hardware and encourage more flexible forwarding to be exposed by the switch firmware.

## Slide 16
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 17
Routing Service: Scenario # 1
106
102
103
105
104
101
101, 102 … 106 are Node Segments allocated out of the SRGB, and bound to the router loopback addresses.
10.10.1.0/24
10.10.6.0/24
Default Routing using Node Segments, ECMP and PHP
10.10.4.0/24
10.10.3.0/24
Global label 106 imposed on pkts dst. to the 10.10.6 subnet
ECMP Paths
Still 106
PHP
Notes: This scenario depicts the default routing service -> SPF with ECMP in a BGP-free core using node-segments.
Consider 6 routers, with their loopback addresses bound to node-segments (or global labels) 101 – 106.
The topology displays two ECMP paths from 101 to 106 >> 101-102-104-106 and 101-103-105-106.
Packets destined to the 10.10.6/24 subnet originating in the 10.10.1/24 subnet will reach router 101. The ‘BGP-next-hop’ for such packets will be router 106.
The BGP-next-hop (106) is resolved into a shortest-path that uses ECMP and the node-segment 106.
The node-segment gets imposed on the packet (source-routing), and then it gets hashed onto the links that go to 102 or 103.
Lets assume this packet takes the upper path.
At 102, the node-segment 106 is still active, and so the label is left alone (or swapped with same label-id) and the packet is forwarded to the shorted path to 106 (which is to 104). Note how SR is different from normal MPLS forwarding (label swap with locally significant labels).
At 104, the node-segment 106 is still active, and so the packet is forwarded to the shortest-path to 106 (which is directly connected). Before sending out of the interface to 106, the label is penultimate-hop-popped (PHP).
At 106, the naked packet (no label) is forwarded via an IP-lookup in the IP table.
Note that forwarding using the IP table is done only at 101 and 106, where as 102 and 104 forward using the MPLS label (aka BGP-free-core).
Also note that this scenario supports L3VPNs (and L2VPNs) using multiple labels like normal MPLS forwarding.

## Slide 18
Routing Service: Scenario # 2
106
102
103
105
104
101
10.10.1.0/24
10.10.6.0/24
Policy Routing
10.10.4.0/24
10.10.3.0/24
Policy#1 – Traffic from .3 to .6 should avoid link X
link X
104
106
Policy#2 – Flow ‘f’ from .1 to .6 should stay in upper plane
Anycast Node Segment 999
102
106
Notes: On this slide we show two scenarios for policy-routing (which do not take the default SPF routing option).
The operator can configure these policies on the controller.
Policy #1 Traffic for 10.10.3/24 to 10.10.6/24 should avoid link X
Normally this traffic would take the shortest path to .6, which is the 103, 105, 106 path.
But avoiding link X (between 105 and 106) means that the traffic should use the 104-106 link.
Thus this traffic should take the shortest ECMP path to 104 and then take the 104-106 link.
This can be implemented with a label stack {104, 106} imposed at 103.
The 104 segment implies that at 103, the packet is hashed over two possible interfaces (ones going to 102 or 105)
Lets assume this packet takes the upper path to 102.
At 102, the active segment is still 104, so 102 determines the shortest path to 104, which is directly connected.
Before exiting, 102 removes the 104 label (PHP).
At 104, the active segment is now 106, and so 104 determined the shortest path to 106, which is directly connected.
Before exiting, 104 removes the 106 label (PHP).
At 106, the packet is looked up in the IP table.
Policy has thus been successfully implemented.
Policy #2 requires that a particular kind of traffic (designated flow ‘f’) from the 10.10.1/24 subnet to 10.10.6/24 subnet, should take the upper of the ECMP paths to the destination. Note that without policy routing, this traffic (like all other traffic) would have taken either of the ECMP paths to the destination (like Scenario # 1).
We can identify flow ‘f’ by using the ACL table at 101, and then override the default routing process, by imposing a label-stack {102, 106} on packets belonging to this flow. Before exiting, 101, the label for 102 is removed.
At 102, the packet is shortest path routed to the active-segment 106, which implies sending the packet to 104.
At 104, the active segment is still 106, so the packet is shortest-path routed to 106. Before exiting, the label 106 is PHP’d.
Note that the anycast-segment 999 is configured on all of the routers in the upper-plane (actually its configured on the controller). It implies that this packet can be sent to any of the routers in the anycast-segment. In this particular example, the packet can be sent to 102 or 104. Using a label-stack {999, 106} would work because 999 implies sending to 102 or 104. But in this sparse topology, this stack will violate the policy in the event of failure of 102. In such a case, the packet will be shortest path-ed to 104, which will use the lower plane (103-105-104), and thus violate the policy. But if the topology included more routers in the upper plane, for example say router 110 (not shown), directly connected to 101, then a label-stack using the anycast-segment {999,106} would work, and it would have the advantage that the policy would not be ‘tied’ to any one router (like 102). On the failure of 102, the flow would automatically reroute to the shortest path to any other router (like 110) that is part of the anycast set, while not violating the policy of staying in the upper plane.

## Slide 19
Routing Service: Scenario # 3
106
102
103
105
104
101
10.10.1.0/24
10.10.6.0/24
10.10.4.0/24
10.10.3.0/24
TE Support: Load-balancing among non-ECMP Paths
Same adjacency segment 12009 assigned to both outgoing links for load-balancing at 102, to 104 or 103
Non-ECMP paths
12009
106
Once at 104 or 103, it’s just SPF to 106
Notes: This is the first of two scenarios that support planned traffic-engineering.
Planned traffic engineering often requires load-balancing traffic across tunnels, that don’t take the normal shortest-path to the destination. For example, in the scenario above, assume two tunnels taking paths 102-104-106 and 102-103-105-106. Clearly these are non-ECMP paths. But traffic arriving at 102, and destined for 106 can still be load-balanced over these paths by using adjacency-segments.
In segment routing, adjacency segments have only local significance. For example, the outgoing links at 102 to 104 and 103 can have the same adjacency-segment 12009 configured on them. 12009 has significance only ay 102, ie. only 102 would have a forwarding entry in its FIB that matches on 12009. The resultant action would be to hash on to the two links that are part of the same adjacency-segment. Once one of the links is chosen, the label 12009 is popped off.
At 103 (or 104), the active segment is 106, and so the packet is shortest-path-ed to 106.

## Slide 20
Routing Service: Scenario # 4
106
102
103
105
104
101
10.10.1.0/24
10.10.6.0/24
TE Support: Explicit Routing
10.10.4.0/24
Desired Explicit Path
Requires label stack:
102
103
105
104
106
102
103
105
Pop 105
Push
104
106
Stitching Segments
Deep-stacks can cause problems in merchant silicon
Cannot push many labels all at once
Can cause loss of entropy if hw cannot read down to L3/L4 headers
Solution: use Segment stitching
Notes: Here is another scenario that supports planned traffic engineering – a strict explicit path.
The path desired takes a circuitous route 102-103-105-104-106. In segment routing it can only be satisfied with a label stack that is 5 labels deep.
Deep label stacks could cause problems in merchant silicon. For example,
We may not be able to push all 5 labels at the same time
Even if we can, the deep stack may result in subsequent routers not being able to ‘read’ the packet down to the L3/L4 headers. When that happens, the packet cannot be hashed based on L3/L4 headers leading to a loss of entropy (although ECMP is not a concern in this particular example).
There are a couple of options open to us to realize this segment route.
One option is to split the explicit path as two segments and stitch them at some point along the path.
For example, 101 imposes a smaller label stack {102, 103, 105}. At 103, when the packet is about to be sent out of the link to 105, the label 105 is popped and the rest of the path is imposed via pushing labels {104, 106}.
Another option is to use label-swapping (not shown). For example, the links along the path have the following adjacency segments defined on them.
@101, link to 102 => 3000
@102, link to 103 => 666
@103, link to 105 => 13002
@105, link to 104 => 971
The packet then could take the following path,
Before 101, impose single label 3000
@ 101, swap 3000 for 666 and send out of link to 102
@ 102, swap 666 for 13002 and send out of link to 103
@ 103, swap 13002 for 971 and send out of link to 105
.. and so on
Note that this is technically not segment routing as it is not ‘source-routed’, but it is a service that can be provided by the routing-service in the controller.
It is also a good example of how you can use software to get around the limitations of hardware.

## Slide 21
Routing Service: Scenario # 5
106
102
103
105
104
101
10.10.1.0/24
10.10.6.0/24
Service Chaining
10.10.4.0/24
Firewall
DPI
Adjacency
Segment 9002
Adjacency
Segment 16555
Desired Chain
103
9002
105
16555
106
Note: Could have used segment-stitching or label-swapping to avoid deep label stack
Notes: This example covers a service chaining scenario that has relevance within or across data-centers. In principle, it can be viewed as the NFVI layer that supports VNFs.
Here services (or VNFs) like firewalls and load-balancers are attached to segment-routers. The operator can define a service chain which goes through two services attached to routers 103 and 105 before being routed to the 10.10.6/24 subnet.
The services are represented as adjacency segments 9002 and 16555 on the links that connect them to routers 103 and 105 respectively. As before, the adjacency segments have relevance only at the routers they are configured on. So when a packet reaches router 103, the active segment (topmost label) is 9002, which makes router 103, remove the label 9002 and send the packet out of link attached to the firewall. When/if the packet returns to 103, the active segment is 105. The router 103 then forwards the packet on the shortest path to 105 (which is the link that is directly connected to 105), and pops off the label ‘105’.
At 105, the active segment is 16555, which means that the router pops off the label 16555 and forwards the packet out of the link that connects it to the DPI engine.
When the packet returns, the active segment is 106, which makes the router 105 send it out of the interface connecting it to 106 (and pop off the label 106).
At 106, the packet is looked up in the IP table.
As in the previous example, we could have used segment-stitching or label-swapping to avoid a deep-label-stack.

## Slide 22
Learn more:
https://wiki.onosproject.org/display/ONOS/Segment+Routing
SPRING-OPEN
Segment Routing on
Bare Metal Hardware

## Slide 23
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 24
PoC Demo @ ONS June‘15
Dell
Dell
Dell
Dell
Dell
Dell
4 racks, 2 servers/rack, Dell 4810 bare metal,
ONOS Cardinal controller cluster
ONOS Controller Cluster
Segment Routed
Fabric Control
SDN controlled
L3 Leaf-Spine Clos fabric.
Dell
Dell

## Slide 25
CORD: Fabric
103

## Slide 26
ECMP Routing

## Slide 27
Control Plane Failure Recovery

## Slide 28
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 29
Leaf
Spine
Leaf
OVS
MAC DA
of Service 2
MAC SA
of S1B
Payload
MAC DA
spine
MAC SA
leaf
SR Label
IP
infrastucture
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
Payload
MAC DA
of S2C
MAC SA
of S1B
Payload
represents
Dst. leaf sw
Dst IP
lookup
SR Label Lookup
Dst IP Lookup
Fabric
Server
Server
From vCPE to S1, or from S1 to S2, etc.
S1B
OVS
S2C
MAC DA
Leaf
MAC SA
OVS
IP
infrastucture
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
Payload
OVS IP addrs.
MAC DA
leaf
MAC SA
spine
IP
infrastucture
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
Payload
Infrastr.
IP
Virtual net
IP
Tunnel decap
Tunnel encap
MAC DA
OVS
MAC SA
leaf
IP
infrastucture
UDP
VXLAN
VNI=S2
MAC DA
of S2C
MAC SA
of S1B
Payload
This example shows how a Service 1 instance (S1B) reaches a Service 2 instance (S2C)

## Slide 30
L2 Bridging withing a Rack

## Slide 31
L3 Across Racks – IP/MPLS

## Slide 32
OLT
vCPE
Leaf
Spine
Leaf
OVS
MAC DA
MAC SA
PON S-Tag
0x88a8
Cust C-Tag
0x8100
Payload
MAC DA
spine
MAC SA
leaf
SR Label
PW Label
MAC DA
MAC SA
PW Label
MAC DA
MAC SA
PON S-Tag
Cust C-Tag
Payload
MAC DA
MAC SA
PON S-Tag
Cust C-Tag
Payload
MAC DA
MAC SA
PON S-Tag
Cust C-Tag
Payload
MAC DA
MAC SA
Cust C-Tag
Payload
vCPE mac
802.1ad
subscriber mac
represents
Dst. server
represents
Dst. leaf sw
Router
macs
Double VLAN lookup
SR Label Lookup
PW Label Lookup
Double VLAN lookup
Can preserve 2 tags, or just C-tag, or remove both tags
Fabric
Server
I/O
From PON to vCPE
This slide presumes that a vCPE has been allocated for a subscriber, where the subscriber can be identified by the double-tag, and the vCPE location has been communicated to the fabric controller
Notes: Plan for single leaf /dual leaf arrangement without any spine?

## Slide 33
802.1ad and Pseudowires

## Slide 34
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 35
Policy Driven Traffic Engineering

## Slide 36
Analytics Driven Traffic Engineering

## Slide 37
Analytics Driven Traffic Engineering

## Slide 39
OpenFlow 1.3
Segment Routing
Leaf-Spine Fabric
Broadcom’s OF-DPA
Analytics driven Traffic Engineering
ONOS & Flow-Objectives
Outline

## Slide 40
A Closer Look at Interoperability
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
Different combinations of
Match-Action Tables form
Different OF 1.3 pipelines
How can a controller manage these differences?
How can an application work across these differences?

## Slide 41
SDN Application
Flow Objectives
OFDPA Driver
Controller
Switch
OpenFlow 1.3
OpenFlow 1.3
Write the app once
without pipeline details
adapt to specific
Pipeline using
device driver
Accton, Quanta (BRCM ASIC)
NoviFlow, Netronome
(NPU/NFP)
Corsa
(FPGA)
Pica8
(BRCM ASIC)
Centec
(ASIC)
SoftRouter Driver
Corsa Driver
Pica8
Driver
Centec Driver
Solution: Flow Objectives API

## Slide 42: Example: Filtering Objective
Filter  only Permit or Deny options
On match fields of packet header
Router port: X
Permit: MAC 1, VLAN 1, IP 1, 2, 3
Permit: MAC 1, VLAN 2, IP 4, 5
Corsa Driver
OF-DPA Driver
T0
mac
T2
port-vlan
T4/5
T6
ip
T0
port
T1
Port-vlan
T2
mac
T4
ip
Flow Objectives

## Slide 43: Example: Next Objective
Next  next hop for forwarding
Similar to OF 1.3 group, but …
NEXT- HOP
Corsa Driver
bkt
Indirect group
NoviFlow & Pica8 Drivers
 Flow-actions
bkt
OF-DPA Driver
Group chain
Flow Objectives

## Slide 44: ONOS Architecture
OpenFlow Provider (1.0, 13)
Netconf Provider
PCEP
Provider
TL-1
Providers
Providers
Core Services (distributed)
Applications
(distributed)
Host Provider
LLDP Provider
Topology Service
Link Service
Device Service
Host Service
Intent
Service
Stats Service
Flow Rule Service
Group
Service
Packet Service
Segment Routing
SDN-IP
BGP Router
Flow Objectives
Driver X
Driver Y
Driver Z
Optical
Mastership Service
I-BGP Speaker/RIB
I-BGP Speaker/RIB

## Slide 45
Summary
CORD Fabric
  Open-source
  Spine-leaf architecture: L3 Clos
  Bare metal hardware
  SDN based – no use of distributed protocols
  OF 1.3 multi-tables & groups
  ONOS cluster controllers
  IP/MPLS network using Segment Routing
  sFlow based analytics for TE of elephant flows
Current Status
  Move to open source hardware i.e OCP/ONL/ONIE/OF-DPA
  Integration with vCPE-vOLT-NFaaS
  Special CORD requirements eg. 802.1ad & Pseudowires
  Pod based deployment requirements eg. BGP/OSPF (vRouter)