## Slide 2: SCIENCE TECHNOLOGY MATHEMATICS
ENGINEERING
Helping to choose a satisfying career
Professor Pat McKeown OBE FREng

## Slide 3: SCIENCE
Science establishes
    knowledge of
    facts about
    laws governing
  the physical universe including the living things it has evolved.
SCIENTIFIC RESEARCH can be
  and finds new facts, new principles and new laws of nature.
theoretical
experimental
SCIENTIFIC RESEARCH
    is mainly what SCIENTISTS DO
    it produces DISCOVERIES
    it is primarily ANALYTICAL

## Slide 4: TECHNOLOGY
dictionary definition: ‘’a useful art or science’’
has been called: ‘’the mother of civilisations’’ because it causes developments that improve standards of living and ‘’liberates mankind from the constraints of the past’’
[new and better tools, food, clothing, water supplies and quality, medicines, transport, communications etc]
the term ‘’technology’’ has recently been hijacked by the media to mean only developments in smart phones, tablets, computer hardware and software systems.

## Slide 5: ENGINEERING
a wide range of advanced technologies
the application of scientific knowledge and best technologies to SOLVE human problems, needs or wants.
essentially a CREATIVE process, it SYNTHESISES solutions to problems and human needs.
it involves
  INVENTION, CREATIVITY AND INNOVATION (‘’the introduction of something new to the market’’)

## Slide 6: Engineers and Engineering
we become engineers because we are fascinated by technology, by why and how things work, by what is technically possible and because we want to CREATE new, useful products and services
the ESSENCE of ENGINEERING is:
    CREATIVITY
    the CONCEPTION and DEFINING of an OBJECTIVE, the HARNESSING of all the requisite RESOURCES, SCIENTIFIC, TECH NICAL, ECONOMIC and HUMAN, to attain the objective, e.g. through Design, Development, Manufacture, Marketing, etc. and then
    ENSURING its subsequent EFFICIENT and RELIABLE APPLICATION to the NEEDS OF THE COMPANY and the COMMUNITY

## Slide 7
Engineering in daily life

## Slide 8
S. Myers QUB March 11, 2009
8
Mobile Phone
SAW Structures
Air Bag
Accelaration Sensors
Cosmetics
TiO2 Nanoparticle
GMR Read Head
Magnetic
Multilayers
Pace Maker
Li-Batteries
New Materials for Energy
Bike Frame
Carbon Fibres
Composite Materials
LED Display
Photonic Materials
GPS Navigation
Functional Materials
Glasses and Coatings
Optical Materials
UV Filter
Artificial Lens
Biocompatible
Polymers
Artificial Hips
Biocompatible
Materials
Exact Time via satellite
Semiconductíng devices
Micro-Batteries
Catalyzer
Nanoparticles
Digital Camera
CCD Chip
Intelligent Credit Card
Integrated Circuits
Notes: 8

## Slide 10
Rolls Royce Trent 900
Gas Turbine Engine

## Slide 11: Airbus A380 now operated by British Airways

## Slide 12: ENGINEERING – in the UK
480,000 engineering businesses
5.6 million people work in UK engineering
587,000 (estimated) engineers needed in manufacturing by 2018
Engineering contributes 20% of the UK’s GDP (income)
– 3X more than the financial sector
A very satisfying career, exercising creativity, rapid change and good pay
ENGINEERING: aerospace; bio-engineering; chemical; civil; electrical; electronic; mechanical; MECHATRONICS; software engineering
INCREASING NATIONAL WEALTH; higher living standards

## Slide 13
Mechatronics in action…e.g. robotics

## Slide 14: Engineering has many disciplines
What is a robot?
  Electrical motors
  Electronics to control the motors
  Mechanical structures with bearings
Is that it?
It needs software to precisely control its behaviour
The software is written by software developers / engineers
….engineers who trained in computer science (or software engineering) courses

## Slide 15: Why software development matters
Software developers created Google, Apple, Facebook, Cisco, Yahoo, Twitter.
These are the biggest and most valuable companies in the world today, and they will continue to grow for many years to come.
In the US, software is a $425 billion industry providing 2.5 million jobs.
By 2023, it is estimated that 10% of the world economy will be in software-related jobs.
The jobs are very well paid: the average software developer is paid more than twice the average professional worker in the US.

## Slide 16: The world needs more software developers!
There are over 11 million software developers in the world today, with over 1 million new software development jobs per year.
There is a shortage of 200,000 software developers in the UK.
A digital divide is growing between those who can program and those who can't.
Ability to code / program is an essential tool to advance capabilities and careers in the arts, (designing ballet choreography!) drama, fashion design, domestic products commerce and many other creative professions.

## Slide 17: Software is more important than ever…
There is a steady growth of demand for software in all aspects of the global economy
Everything now runs intelligently – from our home thermostats to our cars. Software is no longer just on your computer.
It is no longer sufficient to only use software. Participation in a global economy requires creation of new software.
With a strong educational foundation in engineering, we can move from being USERS/CONSUMERS of Software to CREATORS of Software

## Slide 18: MOVE from USER to CREATOR!

## Slide 19: Engineering Nanotechnology - the Ultra Precision Technologies
Professor Pat McKeown OBE FREng
European Society for Precision Engineering
and Nanotechnology

## Slide 21: What is a nanometre?
1 millimetre (mm) ..10-3 metre
1 micrometre (µm) ..10-6 metre
Note: diameter of human hair 80µm; human eye can resolve about 20 µm
1 nanometre (nm) ..10-9 metre....0.000 000 001 metre
1 Ångström (Å) ..10-10 metre Note: this is the “diameter” of a hydrogen atom; large atoms are up to 4 Å diameter
1 picometre (pm) .. 10-12 metre
1 femtometre (fm) SIZE OF A PROTON? .. 10-14 metre

## Slide 22
0.08mm
80,000nm
80um

## Slide 23
Scanning electron microscopy of e-coli on needle tip
2 µm long

## Slide 24
Scanning electron microscopy of cold virus
100 nm
100 nm

## Slide 25: “There’s plenty of room at the bottom” - an invitation to enter a new field of physics by Richard P Feynman
Nanometre scale information storage by electron writing
Integrated circuits for computing
Machines for manipulation of atoms and molecules
http://www.nobel.se/physics/laureates/1965/feynman-bio.html
Talk given on the 20th December 1959 at annual meeting of the
American Physical Society. Published in the February 1960 issue of
Caltech’s Engineering and Science Journal. Discussed:
What is Nanotechnology?

## Slide 27
Nanotechnology ~ definitions
Prof Norio Taniguchi was the first to coin the term Nanotechnology in 1974 “design and manufacture of artefacts in the range 100 nm – 0.1 nm” (McKeown, UK DTI Initiative 1986) “ the study, development and processing of materials devices and systems in which, structure on dimensions of less than 100 nm is essential to obtain the required functional performance”, RoySoc / RAEng 2007

## Slide 28
400 mm dia Axicon for space laser systems

## Slide 29: Diamond cutting / turning process capability……nanotechnology
Ref, Ikawa & Donaldson, circa. 1990
Undeformed chip thickness of 1nm
on amorphous copper
Ref: Technodiamant

## Slide 30
1nm
wavelength

## Slide 31
Large Diamond Turning Machine for producing
X ray Astronomy Mirrors, Cranfield, 1982

## Slide 32
NASA Chandra X Ray Space Telescope

## Slide 33
Cranfield CIDI measuring machines made
for Hughes Danbury for the AXAF “Chandra” X ray space telescope

## Slide 34
The NION Nanocentre Diamond Machining Centre (1990)
the world’s most accurate machine tool of its size

## Slide 35
Mirror 12
Mirror 11
29 mm
Mirror 1
Notes: These very sharp edges are required because of the 98% efficiency reqt – must use ‘dead’ sharp tools

## Slide 36
Next Generation Space Telescope (James Webb Space Telescope)
and the preferred developer of the
complex Spectrometer mirrors?
Cost: $825 million
Launch: 2018
using Ariane 5
Mid Infrared Instrument led by the UK ATC at
the Royal Observatory Edinburgh
MIRI

## Slide 37
Energy Beam Machining…. nanotechnology

## Slide 38
Electron beam writing
Encyclopaedia Britannica on the head of a pin
C. Humphreys Cambridge University
Each letter is made of holes approximately 4nm diameter

## Slide 39
Scanning Tunnelling Microscope (STM)
Piezoelectric actuator (usually a tube) is used to bring sharp metal tip very close to the surface.
Tunnelling current between tip and surface decays exponentially with distance of tip from surface.
Tip is scanned across surface at constant current and signal applied to scanner is recorded.
Scientific American Oct 1989 p 74

## Slide 41: Atom manipulation using scanning probe technology
STM manipulation of 35 Xenon atoms by Eigler and Schweizer. Xe atoms dragged across surface at 4Å/second, total time 22 hours.
Done in liquid He temperature to keep ultra clean from background environment.
“pinning” achieved by increasing current to 50 nano amps
Ref, Nature 344, 524-526 (1990).

## Slide 42
IBM Millipede©

## Slide 43: Practical Aspects of Mechano-Synthesis Using Molecular Assemblers
There are about 1021 C atoms per carat of diamond
With one billion molecular assemblers – operating in parallel, coordinated placement one atom/ms - would take 31 years
Increasing speed of placement to one atom/ms would reduce time to ~ 300 hr
Avogadro’s Number is a BIG number!
Assembling a One Carat Diamond from Carbon Atoms
Notes: Now let’s see why many scientists get heartburn at such proposals.
And, remember all this presumes we have already developed the technology to have on hand a molecular assembler!

## Slide 45
Diameter of telescope (metres)
Increasing size of telescopes
1940
2020
2000
1980
1960
10
20
30
40
1609
1920
1900
E-ELT
Subaru
KECK
VLT
LBT
TMT
HET
Hooker
Hale
WHT
Year
AAT
Galileo
Notes: This graph shows that ground based telescopes are presently going through a period of intense size scale up.
This is after a 50 year period where sensor sensitivity had been the most cost effective means to improve performance.
A key science driver today is the detection of earth like planets, meanings planets to size of earth being located a similar distance from its star as earth is from our sun.
Astronomers considered 30 - 40m scale ground based telescopes will be needed.

## Slide 46: European Extra Large Telescope (ELT) [ the 400th year of the telescope…..Galileo 1609 – 2009 ]
E-ELT
39 metre diameter primary mirror
Aspheric primary mirror design based on 786 x 1.46 metre hexagonal segments
6 metre diameter secondary monolithic deformable mirror adaptive optics
Ref: www.eso.org “operational by 2020” “estimated cost €950m”

## Slide 47: E-ELT primary mirror design having ~ 984 1.46 metre hexagonal segments
Form accuracy : 20 nm RMS, roughness 1 nm RMS
Ref, www.eso.org
1 part in 108 relative precision of form accuracy to size

## Slide 49: Cranfield University BoX® Machine
Ultra-precision, ultra stiff 3 axis freeform grinding machine for large optics up to 2 metres diameter
Truing/dressing
Grinding wheel
Grinding spindle
Metrology frame/optical straightedge
All axes/spindle oil hydrostatic
Laser interferometer / LVDT metrology
Ref: Shore/Morantz (2006)
Lowest control and structural eigenfrequencies > 100 Hz

## Slide 51: Reactive Atomic Plasma Processing
Ar
Ar
CF4
F
F
F
F
F
F
C
C
C
Ar
Ar
Ar
Ar
Ar
Ar
Ar
Ar
Ar
Ar
Excitation Region
Plasma Discharge
Copper coils for Inductively-coupled energy source
Plasma (main) gas
Reactive precursor gas
Si, SiO2, SiC…
Quartz tube
Notes: This is a cross section of the RAP plasma source. We generate a plasma in argon, then inject CF4 into the center of the plasma excitation zone. The plasma rips apart the CF4 and produces a stream of C* and F* atomic radicals. Some of these are ionized, but they neutralize very quickly. The thing that does the etching in our device is neutral atomic radicals of F*.

## Slide 52: Lithography determines lateral dimensions integrated circuits manufacture
Source: ICE
1/1,000 mm

## Slide 53: Lithography is at the heart of i/c chip manufacturing
Repeat 30 to 40 times to build 3 dimensional structures

## Slide 54: 1 part in 108 relative precision of form accuracy to size
Advanced DUV Lithography Systems
employ fused silica optics of up to 250 mm diameter having form accuracy of 2.5nm RMS and roughness < 0.5nm RMS ; 38nm linewidths
……….the ASML TWINSCAN………………..
Ref, Zeiss SMT

## Slide 55: EUV / soft X-ray lithography scheme reflective optics (ASML)
EUV (extreme ultraviolet)
  λ = 13 nm
  linewidth < 35nm (potentially 10nm)
  reflective optics essential (no available EUV transparent materials)
  tilt control of mirrors is highly critical

## Slide 56: NXE:3300B 1st shipment: H1 2012 2nd generation of NXE platform
Specifications
NA = 0.32
Resolution 22 nm 18/16nm with OAI
Overlay 3.5 nm
Productivity 125 wafers per hour
15 mJ/cm2 resist
ASML Veldhoven NL

## Slide 57: We’ve Come a Long Way in 60+ years!
One transistor/cm2
Dec. 23, 1947
Today: Each die contains >500 million transistors!

## Slide 58
Courtesy of Paul Morantz – peacock butterfly (2004)
Thank you for your attention !

## Slide 59
Adaptive optics with deformable
mirrors to correct for the atmospheric distortions experienced when using ground based telescopes viewing images from outer space.
The stellar images were taken by James R. Graham (UCB) with IRCAL on the Lick Observatory 3m.
Normal seeing
With AO

## Slide 60: 2 different source concepts pursued: LPP vs DPP
Laser-Produced Plasma source
CO2 laser
Sn droplet target
Debris mitigation using background gas and/or magnetic fields
Near normal multilayer collector
Pursued by: Gigaphoton, Cymer
Discharge Produced Plasma source
Direct conversion electricity => plasma
Sn liquid
Debris mitigation by set of foils
Grazing incident collector
Pursued by Ushio
Many kW
laser
Near normal
Multilayer collector
Grazing
Ru coated collector
Foil
trap
Sn coated
Rotating disc
Sn droplets
plasma
plasma

## Slide 61: NXE:3100 first shipment Q4 2010 1st generation of the NXE platform
NA=0.25
Sigma=0.8
Resolution 27 nm
SMO=4.5 nm
MMO=7.0 nm
Productivity 60wph at 10mJ/cm2 resist

## Slide 62: Fusion Energy / High Power Lasers
HiPER, RAL
National Ignition Facility, LLNL, USA
(>37500 optics, 7500 > 300mm)
(first 192 laser beams fired successfully 25/02/09)
Laser Mega Joule, CEA, France
(>37500 optics, 7500 > 300mm)
Now planned, HiPER (European) led by Rutherford Appleton, UK)
NIF, LLNL
Notes: 62

## Slide 63: EUV has demonstrated superior imaging compared to 193nm

## Slide 64: EUV / soft X-ray lithography scheme (ASML)

## Slide 65: CREATIVITY ~ Essential for innovation
NON-CONDUCIVE
CONDUCIVE
ATHLETIC
UNIMAGINATIVE
NON-CHALLENGING
DEPENDENT
CONFORMING
INHIBITIVE
PASSIVE
ADEQUATE IQ
PERCEPTIVE
FORCEFUL
DEDICATED
ENERGETIC
EMOTIONALLY EXPRESSIVE
RESULTANT OF CREATIVITY ‘’TENSIONS’’
BROAD INTEREST KNOWLEDGE
SENSITIVE
FLEXIBLE
INTUITIVE
Assessing the likelihood of creativity in a person
PAMcK

## Slide 66: The Management of Innovation
We manage projects/things
‘’enthusing people to a common purpose/objective’’
We LEAD people
ADMINISTRATION TACTICS STRATEGY
ENERGY
ARTICULATE PERSUASIVE
VICARIOUS THRILL OF SEEING OTHERS SUCCEED
JUDGEMENT ANALYSIS SYNTHESIS
MANAGEMENT
LEADERSHIP
TECHNICAL
THE MANAGEMENT TRIANGLE
The essential capabilities of a manager
PAMcK

## Slide 67
67
Ultra-precision engineering

## Slide 68
Shallow trench, approximately 15 nm deep, created by 4 passes

## Slide 69
Probably the first ever image of a extra-solar (exo) planet around
its parent star using AO in the Infra-red (1995); five times the size of Jupiter.
At 2014 we have discovered over 2000 exo planets.
An ELT is essential to directly see earth sized exo-planets near far away stars

## Slide 70: Ultra Precision Machining Technologies
“ductile” mode grinding
0.01 0.1 1 10 100 1000
IBF
RAPT
Fixed abrasive
grinding
Computer
controlled
polishing
MRF
1000
100
10
1
0.1
Removal Rate [mm3/minute]
Roughness [nm] RMS
diamond turning
1
2
3

## Slide 71
Summary
Accuracy capability about 1 part in 108
(metre class surfaces in 10 hours)
BoX® -
Ultra Precision fixed abrasive Grinding & Measuring System, Cranfield
IRP1200 –
Ultra Precision 7 axes
free abrasive polishing
system,
UCL & Zeeko Ltd
RAP –
Re-active atomic plasma
surface figuring system,
Cranfield
Notes: 71

## Slide 72
1000nm
100nm
10nm
1nm
0.1nm
1eV
10eV
100eV
1keV
10keV
13.5nm
92eV
IR
VUV
Soft X-rays
UV
EUV
Hard X-rays
l
E
EUV = 13.5 nm radiation
Generated with plasma source
Extreme UltraViolet Lithography
It requires atomic flat multilayer coated aspheric mirrors
And an all high vacuum system!
Measured shape accuracy: 45 pico metres
=> much less than diameter of Si atom
CxHy = 1x10-9 mbar
H2O = 1x10-7 mbar

## Slide 74
Boltzmann here
Boltzmann Constant Apparatus – acoustic resonator
- defines the value of the temperature scale
Made by Cranfield University for the National Physical Laboratory…. Ultra-precision diamond machining

## Slide 75: New process chain for large optics
Major new UK-based research initiative*
  processing time for large (1+ metre scale) freeform optical surfaces reduced from 100 hours to 10 hours
  3 step process chain
Stage 1
Fixed abrasive Grinding
Stage 3
Reactive Atomic Plasma
1 mm form accuracy
1 μm form accuracy
< 10 nm form accuracy
Stage 2
Computer control polishing
Ultra Precision Surfaces: A New Paradigm – Cranfield/UCL collaboration (2004-2008)
Professor Paul Shore, FREng

## Slide 76: E-ELT requirement for mirrors
Individual segments:
  1 to 2 metres wide, ~20 nm form error
  100s or even 1000s of segments for each primary mirror
Currently takes ~100s hours to machine/polish each segment
100 hours × 2000 segments = 22 years!
Much faster manufacturing process chains are required to produce the segments for proposed ELTs……by 10X at least.