## Slide 1: How to tell your plumbing what to do Protocol Independent Forwarding
Nick McKeown

## Slide 2: With thanks to many others…
ONF PIF: Curt Beckmann (Brocade), Justin Dustzadeh (Huawei), Yatish Kumar (Corsa), Ben Mack-Crane (Huawei), NM, Ben Pfaff (VMware), Jennifer Rexford (Princeton), Haoyu Song (Huawei), Dan Talayco (BFN).
P4: Pat Bosshart (BFN), Dan Daly (Intel), Glen Gibb (BFN), Martin Izzard (BFN), NM, Jennifer Rexford (Princeton), Cole Schlesinger (Princeton), Dan Talayco (BFN), Amin Vahdat (Google), George Varghese (MSFT), David Walker (Princeton).
Special shout out to Navindra Yadav

## Slide 3: OpenFlow is a balancing act
A vendor-agnostic forwarding abstraction, balancing…
  General match+action (hence TCAM model)
  Fixed-function switch ASICs (hence 12 fixed fields)
Balance was necessary because
  Big investments in ASICs and long development cycles requires clear, static guidelines
  Fixed-function ASICs are faster and lower power (ASIC:NPU:CPU = 100:10:1)
Notes: One person’s balance is another’s compromise….

## Slide 4: We have learned
We learned the importance of
  Multiple stages of match+action
  Not changing the specs too fast
  Extensibility
    So OpenFlow can be used in many networks
    So switch vendors can differentiate
Hence, the importance of TTPs.

## Slide 5
Switch OS
Run-time API
Driver
“This is how I process packets”
(TTP)
Fixed-function ASIC

## Slide 6: Programmable switches
Some switches are more programmable than fixed-function ASICs
  CPU (OVS, etc)
  NPU (Ezchip, Netronome etc)
  FPGA (Xilinx, Altera, Corsa)
  Flexible Match+Action ASICs (Intel Flexpipe, Cisco Doppler, Xpliant, …)
“Top-down” These switches let us tell them how to process packets.
Notes: These types of switch have their place: e.g. Hypervisor switches, rack switches, enterprise switches, edge routers, etc.

## Slide 7
Switch OS
Run-time API
Driver
“This is how the switch must process packets”
(PIF)
Programmable Switch

## Slide 8: Why we call it Protocol Independent Forwarding

## Slide 9: Three phases
Phase 0. Initially, the switch does not know what a protocol is, or how to process packets (Protocol Independence).
Phase 1. We tell the switch how we want it to process packets (Configuration).
Phase 2. The switch runs (Run-time).

## Slide 10: Three Goals
Protocol independence
  Configure a packet parser
  Define a set of typed match+action tables
Target independence
  Program without knowledge of switch details
  Rely on compiler to configure the target switch
Reconfigurability
  Change parsing and processing in the field

## Slide 12
Parser
Match+Action Tables
Queues/ Scheduling
Initially, a switch is unprogrammed and does not know any protocols.
The Abstract Forwarding Model
Packet Metadata

## Slide 13
Protocol
Authoring
1
L2_L3.p4
Compile
2
Configure
3
Parser
Match+Action Tables
Queues/ Scheduling
Packet Metadata
TCP
New
IPv4
IPv6
VLAN
Eth
Run-time API
Driver
Switch OS
Run!
4

## Slide 14
Protocol
Authoring
1
L2_L3.p4
Compile
2
Configure
3
Parser
Match+Action Tables
Queues/ Scheduling
Packet Metadata
Run-time API
Driver
Switch OS
Run!
4
OF1-3.p4
OF1.3 Wire Protocol

## Slide 15: P4 Code Examples
Headers and Fields
The Parser
Match+Action Tables
Control flow

## Slide 16: Headers and Fields
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
/* Instance of eth header */
header ethernet_t first_ethernet;
Header Fields: Ethernet
header_type vlan_tag_t {
fields {
pcp : 3;
cfi : 1;
vid : 12;
etherType : 16;
}
}
header vlan_tag_t vlan_tag[NUM];
Header Fields: VLAN
header_type standard_metadata_t {
fields {
ingress_port : 32;
packet_length : 32;
ingress_timestamp : 32;
egress_spec : 32;
egress_port : 32;
egress_instance : 32;
}
}
metadata standard_metadata_t std_metadata;
Metadata

## Slide 17: The Parser
parser parse_ethernet {
extract(ethernet);
return switch(latest.etherType) {
ETHERTYPE_VLAN : parse_vlan;
ETHERTYPE_MPLS : parse_mpls;
ETHERTYPE_IPV4 : parse_ipv4;
ETHERTYPE_IPV6 : parse_ipv6;
ETHERTYPE_ARP : parse_arp_rarp;
ETHERTYPE_RARP : parse_arp_rarp;
}
}
parser parse_ipv4 {
extract(ethernet);
return switch(latest.etherType) {
PROTO_TCP : parse_tcp;
PROTO_UDP : parse_udp;
...
}
}
Parser: Ethernet
Parser: IPv4

## Slide 18: Match+Action Tables
Specifies
  Which fields to examine in each packet
  Actions that may be applied (by rule)
  Table size (optional)
table port_vlan {
reads {
std_metadata.ingress_port : exact;
vlan_tag[OUTER_VLAN].vid : exact;
}
actions {
drop, ing_lif_extract;
}
size 16384;
}
Match+Action Table: VLAN
table urpf_check {
reads {
routing_metadata.bd : ternary;
ipv4.dstAddr : ternary;
}
actions {
urpf_clear, urpf_set;
}
}
Match+Action Table: Unicast RPF

## Slide 19: Actions
Built from primitives
  modify field (packet header or metadata)
  add/remove header
  clone/recirculate
  counter/meter/stateful memory operations
Parallel semantics
/* Ingress logical interface setup */
action ingress_lif_extract(i_lif, bd, vrf, v4term, v6term, igmp_snoop) {
modify_field(route_md.i_lif, i_lif);
modify_field(route_md.bd, bd);
modify_field(route_md.vrf, vrf);
modify_field(route_md.ipv4_term, v4term, 0x1);
modify_field(route_md.ipv6_term, v6term, 0x1);
modify_field(route_md.igmp_snoop, igmp_snoop, 0x1);
}
Actions: LIF Extract

## Slide 20: Control Flow
control ingress {
apply_table(port);
apply_table(bcast_storm);
apply_table(ip_sourceguard);
if (valid(vlan_tag[0])) {
apply_table(port_vlan);
}
apply_table(bridge_domain);
if (valid(mpls_bos)) {
apply_table(mpls_label);
}
retrieve_tunnel_vni();
if (valid(vxlan) or valid(genv) or valid(nvgre)) {
apply_table(dest_vtep);
apply_table(src_vtep);
}
. . . .
}
Control Flow: Ingress

## Slide 21: Use Cases
P4 can be used to describe switches, routers, firewalls, gateways, load-balancers, etc.
Mostly-stateless applications
“P4 is for plumbers”

## Slide 22: P4
P4: Programming Protocol-Independent Packet Processors
ACM CCR. Volume 44, Issue #3 (July 2014)
Pat Bosshart, Glen Gibb, Martin Izzard, and Dan Talayco (Barefoot Networks), Dan Daly (Intel), Nick McKeown (Stanford), Cole Schlesinger and David Walker (Princeton), Amin Vahdat (Google), and George Varghese (Microsoft)
www.p4.org

## Slide 23: How to contribute to P4.org
Contribute to the P4 language spec
Contribute a compiler to your target
Contribute new tools (e.g. debugger)

## Slide 24
Switch
Packet Forwarding Engine
Compiler
Switch
Packet Forwarding Engine
Compiler
P4 Program/Library
The P4 View of the World
Switch
Packet Forwarding Engine
Switch configuration
Compiler
A compiler per target

## Slide 25
P4 Program/Library
The P4 View of the World
Switch
Packet Forwarding Engine
Switch configuration
Compiler
A compiler per target
Intermediate Representation
Front-end compiler
Switch
Packet Forwarding Engine
Switch configuration
Back-end compiler
New ONF open-source project

## Slide 26
Switch
Packet Forwarding Engine
Back-end compiler
Switch
Packet Forwarding Engine
Back-end compiler
Intermediate Representation
High Level Language
Many languages, many targets
New ONF open-source project
Front-end compiler
e.g. P4 program/libraries
Switch
Packet Forwarding Engine
Switch configuration
Back-end compiler

## Slide 27
P4
…
CPU/OVS
NPU
FPGA
FlexPipe
RMT
CPU/Click
GPU
Front-end compiler
Back-end compiler
IR
high level
languages
targets
Doppler

## Slide 28: A Fourth Goal
Protocol independence
Target independence
Reconfigurability
Language independence

## Slide 29: Goals of an IR
Allow new languages above
Compile to many devices below
Uniquely define how packets are to be processed
Keep it simple
Action primitives: minimal “Plumbing Instruction Set (IS)”
Later: Could add DPI IS, Security IS

## Slide 30: Components of IR
Plumbing Instruction Set
Parse graph
Table graph, edges annotated with actions.
Optional: Table graph, annotated with dependencies to allow back-end compiler to exploit concurrency.

## Slide 31: In summary…

## Slide 32
Intermediate Representation
High Level Language
Step 1. Configuration
Switch
Packet Forwarding Engine
Switch configuration
New ONF open-source project
Front-end compiler
e.g. P4 program/libraries
Back-end compiler

## Slide 33
Stage 2. Run-time
Control Plane
OpenFlow
Add, modify, delete
flow entries, etc.
Wire
protocol
OpenFlow
Switch
Packet Forwarding Engine
Run-time API
Run-time API

## Slide 34: Contribute
ONF PIF Open-Source Project
  Approved by ONF Board
  Apache 2.0, open to all
  ONF needs to put open-source governance/license in place (will take a few weeks)
Contribute code to IR
Contribute back-end compiler: (e.g. to OVS, FPGA, NPU, ASIC, …)